## Slide 1
Meeting 2016/07/21 – SaTScan alternatives
SaTScan binary is not enough
No source code
Binary cannot report all clusters  1 cluster / location over the whole period
Alternatives
Analyse partial results
  300m clusters of 1h-5h: ~ 150 events
  Significance ranking is not accurate
Iterative SaTScan: find most significant cluster and “remove” it
  Cannot remove cluster data simply
  Must replace instances by expected count  system of n 2nd degree polynomial equations, n variables
  Every iteration  read counts file ~ 1 min for 1 month hour precision
Theoretical limit: same location weight over time hypothesis
Space-Time Permutation model assumes that relative importance of location does not vary with time
  Alleged source of error on previous experiments
“Adjust day-of-week option”  can it be applied for arbitrary time steps – hour?

## Slide 2
Meeting 2016/07/21 – Clustering & PCA
Clustering
Code of Telang 2014 available
  Grid data
  ST-Clustering density based //DB-SCAN with constraint of persistent shape over time
  LRT significance testing  fitting a Poisson(λ1) in cluster / Poisson(λ2) in surrounding region
First compute clusters, then choose the testing?
  Historical mean, raw threshold…
  Telang 2014 use the same LRT Poisson test for SaTScan and Clustering AD  “fair” comparison
  Problem: Poisson model obviously does not fit traffic TS
Problem: 2 independent dimensions to compare
How to group instances: scan vs clustering
What baseline to use for AD
  would be more rigorous to use the same baseline
  OR “we only implement whole existing techniques”
PCA
Different input matrixes  different correlations
L_t * L  space
  No time correlation captured  Used with counts assumed to be under same law
  Chawla 2012: 2h or 15min-long time windows only
  AD outputs anomalous regions
L * L_t  time
  AD outputs anomalous time steps  out
Karhuven-Loeve transform  space AND time
  More expensive
  No KL ST-AD found yet
Example of matrix L

## Slide 3
Meeting 2016/08/18 – Iterative SaTScan and Telang implementation
1. Iterative SaTScan
Algorithm
Launch SaTscan  outputs most likely cluster
Replace counts of cluster in raw data
  New count = new baseline
Iterate
Works on days, needs to be adapted to hours
Day-data result: Week-end influence // Space-Time permutation hypothesis
  Top 3 clusters are at the same locations during week-end
Day-of-week option in SaTScan for hourly data?

## Slide 4
Meeting 2016/08/18 – Iterative SaTScan and Telang implementation
2. Telang implementation
Parameters
Grid resolution must be precise // homogeneity
Hourly resolution
Time period
Gini threshold – dispersion of clusters
Size of neighborhood : 5x5 cells around cell
Telang typical parameters
720x360 space grid x12 time intervals = 3M cells
Gini threshold = 0,01  Much more homogeneous data than taxi
Telang processing
Adapt data to algorithm from harish raw data
  Smoothing  small grid resolution
  Drop-offs + Pickups
Process to cut expensive
  Threshold on cells = 0,03*mean  cells / 2 // delete cells in the sea, in Central Park…
  Shorten study period to 1 week  cells / 4
Small cells  clustering
Big cells  Point Anomaly detection

## Slide 5
Meeting 2016/08/18 – Iterative SaTScan and Telang implementation
2. Telang implementation
Why struggle for 50m?
Homogeneity
Adapted to the density function computing used for Topology and SaTScan
Grid res | Period | N_Cells | Threshold | Gini | Computing (s) | Avg size
500 | Oct |  | None | 0,001 | Quick | 1,002
500 | Oct |  | None | 0,3 | 150 | 1,37
200 | Oct | 750k | None | 0,01 | NA | 1,02
200 | Oct | 750k | None | 0,1 | 4400 | 1,16
200 | Oct | 750k | None | 0,3 | 9100 | 1,41
200 | Oct | 750k | None | 0,5 | 10500 | 1,58
200 | 25-31 | 190k | 0,03 | 0,1 | 37 | 1,55
50 | 25-31 | 3M | 0,03 | 0,001 | 9000 | 1,006
50 | 25-31 | 3M | 0,03 | 0,1 | 32000 | 1,84
Gini threshold
Not relevant <0,1
Telang uses 0,01
Count threshold
Gets rid of useless cells
++ Average size
Complexity
Linear N_Cells
p^2 * log(p) for p avg cluster size

## Slide 6
Meeting 2016/08/18 – Iterative SaTScan and Telang implementation
2. Telang implementation
Next steps
Currently running: 50m / threshold / 0,3g
Results 0,3 / 0,5
Process data to be more homogeneous?
  Subtract means over week/month/day-of-week